## Slide 1: Using MtConnect Data

## Slide 2: Iteration1
Adapter was set so that the only data received by the agent(mtConnect server was PathPosition)
Used request
  okuma-matata:5000/sample?from=60915?count=100000
  Sampling rate from adapter was 100ms
  Adapter was only outputting pat postion information
  Request pulled position information from the buffer
Example used was HardMoldy_design
Example Workplan was Boeing Profiling
Moldy.stpnc was generated by extending the hardmoldy sample and adding a new workplan
A single workstep was added
  For each point in the sample file apt->GotoXYZ was called

## Slide 3: Results-Original Boeing Profile

## Slide 4: Part Generated via MtConnect Path Position Data

## Slide 5: Observations/Notes
The extreme tool path positions far away form the part are due to sampling before the boeing Profile began to execute on the Okuma Machine
Simulated part will jump Diagonally during rapids as opposed to going up vertically first(Due to sampling rate)
This behavior causes the unusual cut in the simulated model
This failure to perform rapids properly occurs many times as seen by the diagonal tool paths in the simulated part

## Slide 6: Possible Solutions
Increase Sampling rate-May exceed buffer so will need to have information pushed to from the MtConnect server to application every 100000 pts
Determine from MtConnect data when a rapid will occur (determine what stepnc command you are at) and use that to determine when a rapid is occurring
Constantly calculate the current movement vector of the tool, if the distance between two consecutive points(loc1 and loc2) is faster than the feed Threshold*rate*AverageSamplingTime, -> intervene and have next goto location be alpha*vector+location1 then have the following goto location be loc2

## Slide 7: Iteration 2 increased Sampling rate
Increased the sampling rate to 1ms according to adapter settings
Actually closer to 8ms

## Slide 9: Observation
Good Quality

## Slide 10: Possible alterations
Have adapter send other data values to mt connect(current line # etc) and see if there is a significant difference
Determine minimum sampling rate needed for a given feed rate and tolerance

## Slide 11
Iteration 3
10ms according to the adapter

## Slide 13: Iteration4
50ms interval

## Slide 14: Iteration 5
200ms

## Slide 16: Patched #2
Algorithm
  Get a list of all Rapid paths in the original stpnc file
  For all consecutive path position samples
    Compute speed of tool movement form xml
    If tool is moving faster than max feed rate
      Use rapid path from stpnc file and ignore all sample positions with speed>max feed rate
      Correlate rapid path in sample positions with stpnc via chronological order
    Else
      Goto to next coordinate

## Slide 17: Notes
Max feed was hardcoded
Mtconnect data was trimmend to start of program
Manually set units to inches
Manually selecting correct tool
Chronological order used to correlate rapid tool paths
Used trimmed 100ms data

## Slide 19: Patched 3 200ms

## Slide 20
Patch vs raw mtconnect data

## Slide 21: Observations
Uses chronological order of rapids in stpnc to correlate rapids in stpnc to sampled position data
  Intermediate tool path positions during Rapids may vary between machine so matching actual rapid paths with the rapid path in stpnc may be difficult
  Could match start and end point of a rapid path
    Must have a tolerance for position error due to sampling rates and machine tolerance
    Due to close tool paths very similar paths may match if the tolerance is large enough